## Slide 1: My PCB Business Card
Hackware v1.5 (24 Feb 2016)
By: Yeo Kheng Meng (yeokm1@gmail.com)
https://github.com/yeokm1/pcb-name-card
http://yeokhengmeng.com/2015/09/pcb-businessname-card/

## Slide 2: Backstory
(June 2015)
The spelling mistake

## Slide 3: Typical business cards
Plain
Boring
Forgettable
X

## Slide 4: Existing PCB business cards
Logic gates: http://willfj.com/pcb-business-card/
USB keyboard entry: http://eleccelerator.com/usb-business-card/
Light ring: http://www.limpkin.fr/index.php?post/2014/06/16/My-business-card-v2
Flash Drive emulation: http://makezine.com/2012/08/22/pcb-business-card-2/

## Slide 5: Goals of my business card
Be different
Be useful
Appear expensive but not too expensive

## Slide 6: Feature goals
White LED
Ultraviolet LED
Ruler
Quick adding of my contact
  QR code
  NFC (Prototype stage)

## Slide 7: White LED (torch)
Avago Neutral White
PLCC-2 package (3.2 x 2.8 x 1.9mm)
Add 330 ohm resistor to ↓ current
  1mA current

## Slide 8: Ultraviolet LED
Vishay
PLCC-2 package (3.2 x 2.8 x 1.9mm)
405nm (near-UV)
Current usage ~3mA

## Slide 9: UV LED in action

## Slide 10: Switches
C&K Components DPDT slide switch
3mm height

## Slide 11: Young Blue vs Formal Black
Young Blue
CR2016 holders
  2.8mm holder height
  Can tightly-fit CR2025 batteries
NFC storage: 888 bytes
Formal Black (Appears more “atas”)
CR2032 batteries with gold-plated holder
  4.3mm holder height
NFC storage: 1904 bytes

## Slide 12: Why 2 batteries?
Coin cells connected in parallel to reduce current load
High currents reduce overall battery capacity
Two batteries results in >2x single battery life
Source:
Nordic Semiconductor, Sept 2011: High pulse drain impact on CR2032 coin cell battery capacity
http://m.eet.com/media/1121454/c0924post.pdf

## Slide 13: Quick contact adding: QR Code
QR code contains vCard
  BEGIN:VCARD
  N:Yeo;Kheng Meng
  EMAIL:khengmeng@algoaccess.com
  ORG:Algo Access Pte Ltd
  TEL;CELL:+65 97390391
  TITLE:Software/Hardware Engineer
  URL;WORK:http://algoaccess.com
  URL:http://yeokhengmeng.com
  END:VCARD
Generated QR code requires colour inversion
  Black is printed as white in white silkscreen
  Any graphics software including MS Paint can do this
iOS Demo

## Slide 14: Quick contact adding: NFC (1)
  NFC chip contains vCard
    vCard contains extra info as NFC chip memory > 300 bytes for optimum QR Code
  BEGIN:VCARD
  N:Yeo;Kheng Meng
  EMAIL:khengmeng@algoaccess.com
  EMAIL:yeokm1@gmail.com
  ORG:Algo Access Pte Ltd
  TEL;CELL:+65 97390391
  TITLE:Software/Hardware Engineer
  URL;WORK:http://algoaccess.com
  URL:http://yeokhengmeng.com
  URL:https://www.linkedin.com/in/yeokhengmeng
  END:VCARD
Young Blue’s NFC chip
  NXP NTAG216 (NT2H1611)
  HXSON-4/SOT1312-1 package (1.5mm x 2mm)
  888 bytes
  50pf input capacitance
Formal Black’s NFC chip
  NXP NTAG I²C (NT3H1201)
  TSSOP-8 package (5mm x 3mm)
  1904 bytes
  50pf input capacitance

## Slide 15: Quick contact adding: NFC (2)
NFC antenna Design
PCB antenna on TOP layer
Antenna calculations
  F0: 13.56Mhz
  Ctun = Tuning capacitance
  N: Number of turns
  Dout: Outer diameter
  Din: Inner diameter
Antenna fixed values
  35um layer thickness as set by PCB manufacturer
  0.5mm width and gap to ease drawing of traces
  Aim for antenna resonance of 50pF to match NFC chip
  -> Reduce BOM of another tuning capacitor
I dislike calculations so…
Use Panasonic NFC Design Navigator
  http://www.semicon.panasonic.co.jp/en/tool/nfcdesignnavigator/
Antenna calculations source:
http://www.st.com/st-web-ui/static/active/jp/resource/technical/document/application_note/CD00221490.pdf

## Slide 16: Assembly Process 1
Stencil and solder paste

## Slide 17: Assembly Process 2
Hot plate reflow soldering
Hand soldering for battery holders

## Slide 18: Cost (SGD)
Pieces | Young Blue | Formal Black
10 | $15.53 | $17.19
50 | $10.53 | $12.26

## Slide 19: Future work (Concept card)
Only for special case
Sensor suite
  Bosch BME280: temperature and humidity sensor
  Maxim MAX30100: Pulse Oximeter and Heart-Rate Sensor
  Silicon Labs SI1145: UV Sensor
  Texas Instruments TMP007: IR thermometer
OLED screen
Bluetooth Low Energy
  Rigado BMD-300 or Raytac MDBT42 nRF52 module
LIR2450 3.6V rechargeable coin-cell
Microchip MCP73831 battery charging IC

## Slide 20: Sensor breakouts
Maxim MAX30100 breakout
Pulse Oximeter & Heart-Rate Sensor
By MicroElektronika
Bosch BME280 breakout
Temperature & humidity
https://github.com/yeokm1/pcb-bme280-breakout
TMP007 breakout
IR Thermometer
By Adafruit
SI1145 breakout
UV Sensor
By Adafruit

## Slide 21: OLED screen
3cm x 1.5cm
128 x 64 pixels. 0.96” diagonal
Univision Technology UG-2864HSWEG01

## Slide 22: Rigado BMD-300 BLE module
Sample nRF52 module
https://github.com/algoaccess/pcb-breakout-bmd300

## Slide 23: Power source
LIR2450 rechargeable cell
3.6V 120mAh
24.5mm x 5mm
LIR2450 charger
By: theledart
Based on MCP73831

## Slide 24: The End
Hackware v1.5 (24 Feb 2016)
By: Yeo Kheng Meng (yeokm1@gmail.com)
https://github.com/yeokm1/pcb-name-card
http://yeokhengmeng.com/2015/09/pcb-businessname-card/
Help yourselves to the rejected cards